## Slide 1: Homogeneity Edge Detection
William Huibregtse
whuibreg@iu.edu

## Slide 2: Algorithm Overview
For each pixel in the input image, the maximum difference in value from its eight neighbors is calculated
If this value is under the given threshold (suggested to be 30-50 for 8-bit brightness) the outstream pixel is value 0 (no color/zero brightness)
Detects high-to-low or low-to-high brightness edges
Contiguous areas of similar color/brightness will be black

## Slide 3: Algorithm Applications
“Realtime” image/video edge detection possible by streaming pre-processing images through FPGA
Low/High brightness edge boosting when combining edge detection output with original image
Adjustable threshold value does not require re-mapping of Kernel code onto FPGA (Could be used as ASIC chip for increased speed)
Also applies to border pixels with special edge conditions

## Slide 4: Input Data Choreography
Input is single stream of pixels
Currently allows only greyscale (single brightness value), but could easily be modified for RGB input

## Slide 5: Output Data Choreography
Single stream of 8-bit integer brightness values
(A modified version for RGB values would stream out 3 8-bit integer in a vector)

## Slide 6: Expected Performance Gain
Improvements likely significant enough to be usable on high-end image sensors
Significant performance gain from switching to dataflow paradigm
Decreased power dissipation from running computations at the hardware layer